Save the rest of this file as ordinary ASCII text and name it Circular Recess Milling.ngc

(Flat-bottom circular recess milling)
(Ed Nisley KE4ZNU - March 2010)
(Origin = center of recess at surface)
(External clamping far enough away to be unhittable)

(-- Dimensions)

#<_RecessDia>	= 19.5	(recess OD)
#<_RecessDepth> = 12.8	(recess depth below surface)
#<_RecessRad>	= [#<_RecessDia> / 2]

#<_MillDia>	= 9.48	(cutter diameter)
#<_MillSpeed>	= 75	(cutting speed)

#<_StepOver> = [#<_MillDia> / 2]	(max cut width)
#<_MillRad> = [#<_MillDia> / 2]

#<_MaxCutDepth>	= [#<_MillDia> / 4]	(max cut depth)
#<_MaxCutSlope>	= 0.03	(max cut slope)

#<_TraverseZ>	= 1.0	(safe travel height)
#<_TraverseSpeed> = 600	(safe traverse speed)

G40 G49 G80 G90 G92.2 G94 G97 G98	(reset many things)

G55	(working coord system - change as needed)
G21	(metric!)

(-- Figure cut depth per helix pass)

#<_PassCut> = [#<_MaxCutSlope> * 3.142 * [#<_RecessDia> + #<_MillDia>]]

O9000 IF [#<_PassCut> GT #<_MaxCutDepth>]
#<_PassCut> = #<_MaxCutDepth>	(limit max cut for each pass)
O9000 ENDIF

(-- Position to mill first ramp)
( Start at -X,Y=0 side of recess)

G0 Z#<_TraverseZ>

#<CurrentRad> = [#<_RecessRad> - #<_MillRad>]
G0 X[0 - #<CurrentRad>] Y0

G0 Z0	(get to surface)
#<CurrentDepth> = 0.0

F#<_MillSpeed>

(-- mill down layer by layer)

O<layer> DO

#<NextDepth> = [#<CurrentDepth> + #<_PassCut>]	(figure ending level)
O<depthlim> IF [#<NextDepth> GT #<_RecessDepth>]
#<NextDepth> = #<_RecessDepth>
O<depthlim> ENDIF

( ramp down to new Z level, then remove ramp stub)

G2 I#<CurrentRad> Z[0 - #<NextDepth>]
G2 I#<CurrentRad>

( remove central post)

#<NextRad> = [#<CurrentRad> - #<_StepOver>]

O<cleanout> WHILE [#<NextRad> GT 0]

G2 X#<NextRad> I[#<CurrentRad> - [#<_StepOver> / 2]]
G2 X[0 - #<NextRad>] I[0 - #<NextRad>]

#<CurrentRad> = #<NextRad>
#<NextRad> = [#<CurrentRad> - #<_StepOver>]

O<cleanout> ENDWHILE

G2 X#<CurrentRad> I#<CurrentRad>	(clean off stub)

( return to left side to mill next layer)

#<CurrentRad> = [#<_RecessRad> - #<_MillRad>]
G0 X[0 - #<CurrentRad>]

#<CurrentDepth> = #<NextDepth>

O<layer> WHILE [#<CurrentDepth> LT #<_RecessDepth>]

G0 Z#<_TraverseZ>

G0 X0 Y0

M2