Save the remainder of this file as plain text: postmill.ngc

(Post milling)
(Ed Nisley KE4ZNU - Feb 2010)
(Origin = center of post at surface)
(Double-stick tape holding acrylic sheet to sacrificial plate)

(-- Dimensions)

#<_PostDia>	= 0.300	(post OD)
#<_PostRad>	= [#<_PostDia> / 2]

#<_Thickness>	= 0.120	(sheet thickness)

#<_MillDia>	= 0.250	(cutter diameter)
#<_MillSpeed>	= 15	(cutting speed)

#<_MaxCutDepth>	= [#<_MillDia> / 5]	(max cutting depth)
#<_MaxCutSlope>	= 0.04	(max cutting slope)

#<_TraverseZ>	= 0.300	(safe travel height)
#<_TraverseSpeed> = 25	(safe traverse speed)

G20	(inches!)

(-- Figure cut depth per helix pass)

#<_PassCut> = [#<_MaxCutSlope> * 3.142 * [#<_PostDia> + #<_MillDia>]]

O9000 IF [#<_PassCut> GT #<_MaxCutDepth>]
#<_PassCut> = #<_MaxCutDepth>	(limit max cut for each pass)
O9000 ENDIF

(-- Set up cutter comp)

G0 Z#<_TraverseZ>

G0 X[0 - 3 * #<_PostRad>] Y0	(get to entry point)

G42.1 D#<_MillDia>
G2 X[0 - #<_PostRad>] I#<_PostRad> F#<_TraverseSpeed>

(-- cut down through sheet)

#<CurrentZ> = 0.0

G0 Z#<CurrentZ>

F#<_MillSpeed>

O1000 DO

#<NextZ> = [#<CurrentZ> - #<_PassCut>]	(figure ending level)

G3 I#<_PostRad> Z#<NextZ>	(once around)

#<CurrentZ> = #<NextZ>

O1000 WHILE [#<CurrentZ> GT [0 - #<_Thickness>]]

G3 I#<_PostRad>	(clear final ramp)

G40	(comp off)

G0 Z#<_TraverseZ>
G0 X0 Y0

M2